## Slide 1: Digital Design with Verilog

## Slide 3: Agenda
Introduction
Designing with Verilog
Finite State Machines Review
Verilog for Synthesis

## Slide 4: Introduction

## Slide 5
always @(posedge clk)
begin
x = b & c;
y = a | x;
end
Before 1990 (synthesis)
HDL description

## Slide 6
So we are going to talk about design
And how to use an HDL language to design?

## Slide 7: What is HDL?
Hard & Difficult Language?
  No, means Hardware Description Language
High Level Language
  To describe the circuits by syntax and sentences
  As oppose to circuit described by schematics
  Allows designers to model the concurrency of process found in hardware
Widely used HDLs
  Verilog – Similar to C
  SystemVerilog – Similar to C++
  VHDL – Similar to PASCAL

## Slide 8: What is HDL?
Hardware Description Language
High Level Language
  To describe the circuits by syntax and sentences
  As oppose to circuit described by schematics
  Allows designers to model the concurrency of process found in hardware
Widely used HDLs
  Verilog – Similar to C
  SystemVerilog – Similar to C++
  VHDL – Similar to PASCAL

## Slide 9: Purpose of HDLs
Purpose of Hardware Description Languages
  Capture design in RTL form
    i.e. all registers specified
  Use to simulate designs so as to verify correctness
  Pass through synthesis tools to obtain reasonable optimal gate-level design that meets timing
  Design productivity
    Automatic synthesis
    Capture design as RTL instead of schematic
    Reduces time to create gate level design by an order of magnitude
Synthesis
  Basically, a Boolean combinational logic optimizer that is timing aware

## Slide 10: Verilog
1984:
Verilog was developed by Gateway Design Automation as a proprietary language for logic simulation.
1989:
Gateway was acquired by Cadence
1990:
Verilog was made an open standard under the control of Open Verilog International.
1995:
The language became an IEEE standard (IEEE STD 1364) and was updated in 2001 and 2005.
Notes: One limitation: Description of digital systems only
2005 It fix some problems like for example naming a the generate statements

## Slide 11: SystemVerilog
SystemVerilog is the industry's first unified hardware description and verification language
Started with Superlog language to Accellera in 2002
Verification functionality (base on OpenVera language) came from Synopsys
In 2005 SystemVerilog was adopted as IEEE Standard (1800-2005). The current version is 1800-2009
Notes: Accellera Systems Initiative is an independent, not-for profit organization dedicated to create, support, promote, and advance system-level design, modeling, and verification standards for use by the worldwide electronics industry

## Slide 12: IEEE-1364 / IEEE-1800
Verilog 2005 (IEEE Standard 1364-2005) consists of minor corrections, spec clarifications, and a few new language features
SystemVerilog is a superset of Verilog-2005, with many new features and capabilities to aid design-verification and design-modeling
Notes: SystemVerilog
- adds data structures and assertions for design
- provides advanced verification and modeling features
SystemVerilog design features details
New data types
logic
Multidimensional packed arrays
Enumerated
Structure and unions
Unique/priority if/case
Procedural blocks (always_comb, always_ff, always_latch)
Interfaces
Classes
Assertions
If we see verilog as a subset of System verilog, te first step to lear SV will be lear Verilog

## Slide 13: Simulation and Synthesis
The two major purposes of HDLs are logic simulation and synthesis
  During simulation, inputs are applied to a module, and the outputs are checked to verify that the module operates correctly
  During synthesis, the textual description of a module is transformed into logic gates
Circuit descriptions in HDL resemble code in a programming language. But the code is intended to represent hardware
Not all of the Verilog commands can be synthesized into hardware

## Slide 14: Simulation and Synthesis
Our primary interest is to build hardware, we will emphasize a synthesizable subset of the language
Will divide HDL code into synthesizable modules and test bench (simulation)
  The synthesizable modules describe the hardware.
  The test bench checks whether the output results are correct (only for simulation and cannot be synthesized)

## Slide 15: Types of modeling
Behavioral
  Models describe what a module does.
  Use of assignment statements, loops, if, else kind of statements
Structural
  Describes the structure of the hardware components
  Interconnections of primitive gates (AND, OR, NAND, NOR, etc.) and other modules
Counter
If (rst)
cnt = 0;
else
cnt = cnt+1;
cnt [0:3]
clk
rst
Notes: As I said Verilog is a hardware description lenguage that describe circuits, we can describe/model in 2 ways
Behaivoral
Structural
(the mix on those styles is usually call RTL)

## Slide 16: Behavioral - Structural
module cter (
input rst, clock,
output reg [1:0] count);
always@(posedge clock)
begin
if (rst) count = 0;
else count = count+1;
end
endmodule
module cter ( rst, clock, count );
output [1:0] count;
input rst, clock;
wire N5, n1, n4, n5, n6;
FD1 U0 (.D(N5), .CP(clock),
.Q(count[0]), .QN(n6));
FD1 U1 (.D(n1), .CP(clock),
.Q(count[1]), .QN(n5));
MUX21 U2 (.A(N5), .B(n4),
.S(n5), .Z(n1) );
NR2 U3 (.A(n6), .B(rst),
.Z(n4));
NR2 U4 (.A(count[0]), .B(rst),
.Z(N5));
endmodule
Behavioral
Structural
Notes: Combination can be treat as RTL file or description

## Slide 17: From this…

## Slide 18: To this…
To This
Notes: Sorry about the

## Slide 19: Designing with Verilog

## Slide 20: Design Mantras
One clock, one edge, Flip-flops only
Design BEFORE coding
Behavior implies function
Clearly separate control and datapath

## Slide 21: Basic Verilog Constructs
Flip Flop
  Behavior
    For every positive edge of the clock Q changes to become equal to D
Write behavior as “code”
always @()
  Triggers execution of the following code block
  () called “sensitivity list”
    Describes when execution triggered

## Slide 22: Mantra # 3
Behavior implies function
  Determine the behavior described by the Verilog code
  Choose the hardware with the matching behavior
Code behavior
  Q re-evaluated every time there is a rising edge of the clock
  Q remain unchanged between rising edges
This behavior describes an edge-triggered Flip-Flop
always @(posedge clk)
Q <= D;

## Slide 23: More Examples
What is the behavior and matching logic for this code fragment?
What is the behavior and code for this schematic?
always @(clk or D)
if (clock) Q >= D;

## Slide 24: Flip - Flops
Every variable assigned in a block starting with
becomes the output of an edge-triggered flip –flop
This is the only way to build flip-flops
always @(posedge clk) or
always @(negedge clk)

## Slide 25: Combinational Logic
Combinational logic example
How would you describe the behavior of this function in words?
And in code?

## Slide 26: Behavior  Function
All logical inputs in sensitivity list
If, else  multiplexor
Behavior: whenever input changes, out = mux XOR or OR
Same behavior as combinational logic
always @(a or b or c)
if (a) out = b ^ c;
else out = b | c;

## Slide 27: Procedural blocks
Statement block starting with an “always@” statement is called a procedural block
Statements in block are generally executed in sequence (i.e. procedurally)

## Slide 28: Alternative Coding Style for Combinational Logic
Verilog has a short hand way to capture combinational logic
Called “continuous assignment”
LHS re-evaluated whenever anything in RHS changes
same as
assign out = a ? b ^ c : b | c;
f = a ? d : e;
if (a) f = d else f = e;

## Slide 29: Input Logic to Flip-Flops
Can include some combinational logic in FF procedural block
Behavior  function
  Out is reevaluated on every clock edge  output of FF
  If; else  MUX
always @(posedge clk)
if (c)
out <= b;
else
out <= a;

## Slide 30: RTL Coding Styles
Three coding styles
  always @(???edge clock)  FF and input logic
  always @(*)  Combinational logic (CL)
  assign a = ….  Combinational logic (CL)
The hard part is not coding but design

## Slide 31: Always Design Before Coding
Must code at register transfer level
Register and “transfer” (combinational) logic must be worked out before coding can start

## Slide 32: Design Before Coding
Automatic synthesis does not relieve you of logic design
it does relieve you of
  Logic optimization
  Timing calculations and control
  In many cases, detailed logic design
If you don’t design before coding, you are likely to end up with the following
  A very slow clock (long critical path)
  Poor performance and large area
  Non-synthesizable Verilog
  Many HDL lint errors

## Slide 33: Avoid Temptation
Temptation # 1
  “Verilog looks like C, so I’ll write the algorithm in C and turn it into Verilog with a few always @ statements”
  Usual results: Synthesis problems, unknown clock level timing, too many registers
Temptation # 2
  “I cant work out how to design it, so I’ll code up something that looks right and let Synthesis fix it”
  Usual result: Synthesis does not fix it
Temptation #3
  “Look at these neat coding structures available in Verilog, I’ll write more elegant code and get better results”
  Usual result: Synthesis problems for neophytes
  Better logic, not better code, gives a better design

## Slide 34: Design Before Coding – Steps in Design
Work out the hardware algorithm and overall strategy
Identify and name all registers (flip – flops)
  Determine system timing while doing that
Identify the behavior of each “cloud” of combinational logic
Translate design to RTL
Verify design
Synthesize design

## Slide 35: Procedural Blocks
Code of the type
is referred as procedural code
  Statements between begin and end are executed procedurally, or in order
  Variables assigned (on the left hand side) in procedural code must be of a register data type. Type reg is used
    It does not mean it is a register or a FF
  The procedural block is executed when triggered by the always@ statement
  The statement in parenthesis are referred to as the sensitive list
always @(input1 or input2 or …) begin
if or case statements
end

## Slide 36: Blocking vs. Non-Blocking
Why use <= to specify flip-flops
Blocking
  Assignment of C blocked until A = B completed  They executed in sequence
Non Blocking
  Assignment of C not blocked until A = B completed  They executed in parallel
begin
A = B;
C = D;
end
begin
A <= B;
C <= D;
end

## Slide 37: Blocking vs. Non-Blocking
begin
a = b;
c = a;
end
begin
a <= b;
c <= a;
end
Blocking
Non-Blocking

## Slide 38: Blocking Statements
Hand execute the following
Results?
//test fixture
initial begin
a = 4’h3; b = 4’h4;
end
//code
always @(posedge clock)
c = a + b;
d = c + a;
end

## Slide 39: Non Blocking Statements
Contrast it with this code
Results?
//test fixture
initial begin
a = 4’h3; b = 4’h4; c = 4’h2;
end
//code
always @(posedge clock)
c <= a + b;
d <= c + a;
end

## Slide 40: Blocking vs. Non Blocking
Which describes better what you expect to see?
  Non blocking assignment
Note
  Use non blocking for flip flops
  Use blocking for combinational logic
    Logic can be evaluated in sequence
    Not synchronized to clock
  Don’t mix them ion the same procedural block

## Slide 41: Common Problems and Fixes
Unintentional latches
  Detected after reading the design
  How to fix: make sure every variable is assigned for every way code is executed (except for flip flops)
  If unfixed: you can have glitches on “irregular clock” to latch cause set up and hold problems in actual hardware (transient failures)
always @(a or b) begin
if (a) c = ~b;
else d = |b;
end
Problem code

## Slide 42: Common Problems and Fixes
Incomplete sensitivity list
  Detected after reading the design
  How to fix: all logic inputs have to appear in sensitivity list or use always @(*) (Verilog 2001)
  If unfixed: since simulation results won’t match what actual hardware will do, bugs can remain undetected
always @(a or b) begin
if (a) c = b ^ a;
else c = d & e;
f = c | a;
end
Problem code

## Slide 43: Common Problems and Fixes
Unintentional wired-or logic
  Detected after reading the design, variables cannot be assigned in more than one block
  How to fix: redesign hardware so that every signal is driven by only one piece of logic (or redesign s a tri-state buf if that is the intention)
  If unfixed: unsynthesizable, this is a symptom of not designing before coding
always @(a or b)
c = |b;
always @(d or e)
c = ^e;
Problem code

## Slide 44: Common Problems and Fixes
Improper startup
  Cannot be detected
  How to fix: make sure don’t cares are propagated
  If unfixed: possible undetected bug in reset logic
always @(posedge clock)
if (a) q <= d;
Always @(q or e)
case (q)
0: f = e;
default: f = 1;
endcase
Problem code

## Slide 45: Common Problems and Fixes
Feedback in combinational logic
  Either results in
    Latches, when the feedback path is short
    Timing Arcs when feedback path is convoluted
  Fix by redesigning logic to remove feedback
    Feedback can only be through FFs
WRONG
OK

## Slide 46: Common Problems and Fixes
Incorrect use of FOR loops
  Only correct use is to iterate through an array of bits
  If in doubt, do not use it
Unconstrained timing
  To calculate permitted delay, synthesis must know where the FFs are
  If you have a path from input port to output port that does not path through a FF, synthesis cannot calculate timing
  To fix: revisit modules partitioning (see later) to include FFs in all paths

## Slide 47: Finite State Machines Review

## Slide 48: Finite-State machine
Abstraction
Notes: Synchronous sequential circuits can be drawn in the forms shown in
Figure 3.22. These forms are called finite state machines (FSMs). They get
their name because a circuit with k registers can be in one of a finite number
(2k) of unique states.

## Slide 49: Finite-State machine Abstraction
Clocked Storage Elements: Flip-Flops and Latches should be viewed as synchronization elements, not merely as storage elements !
Their main purpose is to synchronize fast and slow paths:
  Prevent the fast path from corrupting the state
Function of clock signals is to provide a reference point in time when the FSM changes states

## Slide 50: FSM - Types
Moore machine
  Outputs depend solely on state vector (simplest to design)
Mealy machine
  Outputs depend on inputs and state vector (only use it if smaller or faster machines are needed)

## Slide 51: Finite-State machine
State Changes
Notes: Si extendemos el el diagrama de FSM en el tiempo tenemos un diseño pipeline
El diagrama se asume que el cambio de estado se produce cuando la señal clock, cambia de “0” a “1”, en este caso un FF
Como se puede ver sin la señal de reloj no se puede precisar cuando se produce un cambio de estado
Hay sistemas donde el cambio de estado se produce por el cambio de la data (y no por la señal de reloj) se llaman sistemas asíncronos, se han desarrollado microprocesadores para operar de manera asíncrona con pequeñas ventaja en el consumo de energía, pero solo trataremos sistemas síncronos

## Slide 52: Finite-State machine
Critical Path
Critical path is defined as the chain of gates in the longest (slowed) path thought the logic
Notes: En muchos caso el tiempo que toma la lógica combinatoria es mucho mayor y no alcanza a propagarse a la entrada de los clocked storage elements para el siguiente estado
En este case la máquina no cumple el critical path requierement y la FSM fallará en su operación, por que el cambios en la señales de entrada no tendrán el efecto
El tiempo para realizar el cambio de estado es muy corto para los cambios de la señales de entrada se propaguen (critical-path violation)
Critical path: se define como la cadena de compuertas en el path, mas largo (lento) que produce que una señal tope un cierta cantidad de tiempo para propagar la señal de la entrada a la salida

## Slide 53: FSM Implementation
A level-to-pulse converter produces a single-cycle pulse each time its input goes high.
In other words, it’s a synchronous rising-edge detector.
Sample uses:
  Buttons and switches pressed by humans for arbitrary periods of time
  Single-cycle enable signals for counters
Design example
Whenever input L goes from low to high...
...output P produces a single pulse, one clock period wide.
Level to Pulse Converter
P
L
CLK
Notes: Show all the steps that need to be done

## Slide 54: FSM Implementation
State Diagram (Moore implementation)
Current State |  | In | Next State |  | Out
S1 | S0 | L | S1+ | S0+ | P
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0
Notes: Moore implementation
Generamos un diagrama de transición y con esto la tabla de estados
Tenemos que generara una tabla para que indica que se tiene que poner en la entrada de los FF para que cambien de un estado a otro
En la tabla se muestra estado presente y el estado actual
Para cada tipo de FF tenemos que hacer una tabla para cada una de las entradas de los FF, para hacer que cambien a una cierta entrada, se responde la pregunta ¿Qué se tiene que poner en la entrada del FF para que se logre el cambio deseado?
Se genera una nueva columna que muestra que es lo que se tiene en la entrada de los FF

## Slide 55: FSM Implementation
Logic implementation
Flip-Flops
Comb Logic
Comb Logic
P
L
S+
S
L\S1S0 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | X
1 | 0 | 1 | 1 | X
L\S1S0 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | X
1 | 1 | 1 | 1 | X
S0\S1 | 0 | 1
0 | 0 | X
1 | 1 | 0
For S1+:
For S0+:
For P:
Notes: Definir el tipo de FF
Para el caso del FF D:
- se utiliza el estado presente y las entrada y se completa el M-K con los valores del estado futuro
Para el caso FF T
- se genera una tabla de entradas para que el FF cambie al estado deseado
- se utiliza el estado presente y las entrada y se completa el M-K con la nueva columna con las entradas del FF

## Slide 56: FSM Implementation
Since outputs are determined by state and inputs, Mealy FSMs may need fewer states than Moore FSM implementations
Mealy implementation
Pre State | In | Next State | Out
S | L | S+ | P
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 1 | 1 | 0
Notes: Los cambios en la salidas son inmediatas dado que las salidas dependen tambien de las entradas
En este caso FSM es mas simple pues solo se recuerda el estado anterior de L

## Slide 57: FSM Implementation
Remember that the difference is in the output:
  Moore outputs are based on state only
  Mealy outputs are based on state and input
  Therefore, Mealy outputs generally occur one cycle earlier than a Moore:
Compared to a Moore FSM, a Mealy FSM might...
  Be more difficult to conceptualize and design
  Have fewer states
Moore/Mealy trade-off
Moore
Mealy
Notes: The implementation, needs some extra work to optimize the implementation
Right selection of the state coding
Right selection of the registers
Eliminate the redundant states

## Slide 58: HDL FSM Implementation
Straight encoding of states
S0=“00” S1=“01” S2=“10” S3=“11”
For n states, there are [log2(n)] flip-flops needed
This gives the least numbers of flip-flops
Good for “Area” constrained designs
Number of possible illegal states = 2[log2(n)]–n
Drawbacks:
  Multiple bits switch at the same time = Increased noise and power
  Next state logic is multi-level = Increased power and reduced speed
Binary Encoding
Notes: Un a de las cosas que hicimos en la parte anterior fue definir
[] Escalón

## Slide 59: HDL FSM Implementation
Encoding using a gray code where only one bit switches at a time
S0=“00” S1=“01” S2=“11” S3=“10”
For n states, there are [log2(n)]flip-flops needed
This gives low power and noise due to only one bit switching
Good for “power/noise” constrained designs
Number of possible illegal states = 2[log2(n)]–n
Drawbacks:
  The next state logic is multi-level = Increased power and reduced speed
Gray-Code Encoding
Notes: [] Escalon superior

## Slide 60: HDL FSM Implementation
Encoding one flip-flop for each state
S0=“0001” S1=“0010” S2=“0100” S3=“1000”
For n states, there are n flip-flops needed
The combination logic is one level (i.e., a decoder)
Good for speed
Especially good for FPGA due to “Programmable Logic Block”
Number of possible illegal states = 2n–n
Drawbacks:
  Takes more area
One-Hot Encoding

## Slide 61: HDL FSM Implementation
Typically trade off Speed, Area, and Power
State Encoding Trade-Offs
One-Hot
Gray
Binary
Area
Speed
Power

## Slide 62: HDL FSM Implementation
The FSM coding style should be easily modified to change state encodings and FSM styles
The coding style should be compact
The coding style should be easy to code and understand
The coding style should facilitate debugging
The coding style should yield efficient synthesis results
FSM Coding goals
Notes: Three different FSM designs will be examined
Un a de las cosas que hicimos en la parte anterior fue definir un codificacion de los estados, veamos las posibles opciones y sus caracteristicas

## Slide 63: HDL FSM Implementation
One of the best Verilog coding styles
Code the FSM design using two always blocks,
  One for the sequential state register
  One for the combinational next-state and combinational output logic.
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= IDLE;
else state <= next;
always @(state or in1 or in2) begin
next = 2'bx; out1 = 1'b0;
case (state)
IDLE : if (in1) next = BBUSY;
else next = IDLE;
BBUSY: begin
out1 = 1'b1;
if (in2) next = BBUSY;
else next = BFREE;
end
//...
endcase
end
Two Always Block FSM Style (Good Style)
Notes: Parameters are used to define state encodings instead of the Verilog `define macro definition construct[3].
The sequential always block is coded using nonblocking assignments.
The combinational always block sensitivity list is sensitive to changes on the state variable and all of the inputs referenced in the combinational always block.
Assignments within the combinational always block are made using Verilog blocking assignments.
Default output assignments are made before coding the case statement (this eliminates latches and reduces the amount of code required to code the rest of the)
Placing a default next state assignment on the line immediately following the always block sensitivity list is a very efficient coding style
- This is a useful technique to debug state machine designs, plus the X's will be treated as "don't cares" by the synthesis tool.

## Slide 64: HDL FSM Implementation
Use parameters to define state names because the state name is a constant that applies only to the FSM module
The sequential always block is coded using nonblocking assignments, in order to module sequential logic (accurately simulate hardware)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= IDLE;
else state <= next;
always @(state or in1 or in2) begin
next = 2'bx; out1 = 1'b0;
case (state)
IDLE : if (in1) next = BBUSY;
else next = IDLE;
BBUSY: begin
out1 = 1'b1;
if (in2) next = BBUSY;
else next = BFREE;
end
//...
endcase
end
Two Always Block FSM Style (Good Style)
1
2
Notes: 2: this help to accurately simulate hardware

## Slide 65: HDL FSM Implementation
The combinational always block sensitivity list is sensitive to changes on the state variable and all of the inputs referenced in the combinational always block.
Assignments within the combinational always block are made using Verilog blocking assignments, in order to module sequential logic (accurately simulate hardware)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= IDLE;
else state <= next;
always @(state or in1 or in2) begin
next = 2'bx; out1 = 1'b0;
case (state)
IDLE : if (in1) next = BBUSY;
else next = IDLE;
BBUSY: begin
out1 = 1'b1;
if (in2) next = BBUSY;
else next = BFREE;
end
//...
endcase
end
Two Always Block FSM Style (Good Style)
3
4
Notes: 3:

## Slide 66: HDL FSM Implementation
Default output assignments are made before coding the case statement (this eliminates latches and reduces the amount of code required to code the rest of the)
Placing a default next state assignment on the line immediately following the always block sensitivity list is a very efficient coding style
Two Always Block FSM Style (Good Style)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= IDLE;
else state <= next;
always @(state or in1 or in2) begin
next = 2'bx; out1 = 1'b0;
case (state)
IDLE : if (in1) next = BBUSY;
else next = IDLE;
BBUSY: begin
out1 = 1'b1;
if (in2) next = BBUSY;
else next = BFREE;
end
//...
endcase
end
5
6
Notes: Placing a default next state assignment on the line immediately following the always block sensitivity list is a very efficient coding style
- This is a useful technique to debug state machine designs, plus the X's will be treated as "don't cares" by the synthesis tool.

## Slide 67: HDL FSM Implementation
One of the most common FSM coding styles in use today
  It is more verbose
  It is more confusing
  It is more error prone
(comparable two always block coding style)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state;
always @(posedge clk or negedge rst_n)
if (!rst_n) begin
state <= IDLE;
out1 <= 1'b0;
end
else begin
state <= 2'bx; out1 <= 1'b0;
case (state)
IDLE : if (in1) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= IDLE;
BBUSY: if (in2) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= BFREE;
endcase
end
One Always Block FSM Style (Avoid This Style!)
Notes: A declaration is made for state. Not for next.
There is just one sequential always block, coded using nonblocking assignments.
The state assignments do not correspond to the current state of the case statement, but the state that case statement is transitioning to. This is error prone (but it does work if coded correctly).
All outputs will be registered (unless the outputs are placed into a separate combinational always block or assigned using continuous assignments). No asynchronous Mealy outputs can be generated from a single synchronous always block.

## Slide 68: HDL FSM Implementation
A declaration is made for state. Not for next.
The state assignments do not correspond to the current state of the case statement, but the state that case statement is transitioning to. This is error prone (but it does work if coded correctly).
One Always Block FSM Style (Avoid This Style!)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state;
always @(posedge clk or negedge rst_n)
if (!rst_n) begin
state <= IDLE;
out1 <= 1'b0;
end
else begin
state <= 2'bx; out1 <= 1'b0;
case (state)
IDLE : if (in1) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= IDLE;
BBUSY: if (in2) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= BFREE;
endcase
end
1
2
Notes: Since there is no next state, the state assignment, correspond the next state

## Slide 69: HDL FSM Implementation
There is just one sequential always block, coded using nonblocking assignments. Difficult to track the changes
All outputs will be registered. No asynchronous Mealy outputs can be generated from a single synchronous always block.
One Always Block FSM Style (Avoid This Style!)
parameter [1:0]
IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state;
always @(posedge clk or negedge rst_n)
if (!rst_n) begin
state <= IDLE;
out1 <= 1'b0;
end
else begin
state <= 2'bx; out1 <= 1'b0;
case (state)
IDLE : if (in1) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= IDLE;
BBUSY: if (in2) begin
state <= BBUSY;
out1 <= 1'b1;
end
else state <= BFREE;
endcase
end
3
4
Notes: 3 difficult to see when the varaibles changes it values

## Slide 70: HDL FSM Implementation
parameter [1:0] IDLE=0, BBUSY=1,BFREE=2;
reg [2:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= 3’b001;
else state <= next;
always @(state or in1 or in2) begin
next = 3’b000; out1 = 1'b0;
case (1’b1) //ambit synthesis case full, parallel
state[IDLE] : if (in1) next[BBUSY] = 1’b1;
else next[IDLE] = 1’b1;
state[BBUSY]: begin
out1 = 1'b1;
if (in2) next[BBUSY] = 1’b1;
else next[BFREE] = 1’b1;
end
//...
endcase
end
One-hot FSM Coding Style (Good Style)
Efficient (small and fast) One-hot state machines can be coded using an inverse case statement

## Slide 71: HDL FSM Implementation
parameter [1:0] IDLE=0, BBUSY=1, BFREE=2;
reg [2:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= 3’b001;
else state <= next;
always @(state or in1 or in2) begin
next = 3’b000; out1 = 1'b0;
case (1’b1) //ambit synthesis case full, parallel
state[IDLE] : if (in1) next[BBUSY] = 1’b1;
else next[IDLE] = 1’b1;
state[BBUSY]: begin
out1 = 1'b1;
if (in2) next[BBUSY] = 1’b1;
else next[BFREE] = 1’b1;
end
//...
endcase
end
Index into the state register, not state encodings
One-hot requires larger declarations
State reset, set to 1 the IDLE bit
Next state assignment must make all-0's
Onehot FSM Coding Style (Good Style)
1
2
3
4

## Slide 72: HDL FSM Implementation
parameter [1:0] IDLE=0, BBUSY=1, BFREE=2;
reg [2:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= 3’b001;
else state <= next;
always @(state or in1 or in2) begin
next = 3’b000; out1 = 1'b0;
case (1’b1) //ambit synthesis case full, parallel
state[IDLE] : if (in1) next[BBUSY] = 1’b1;
else next[IDLE] = 1’b1;
state[BBUSY]: begin
out1 = 1'b1;
if (in2) next[BBUSY] = 1’b1;
else next[BFREE] = 1’b1;
end
//...
endcase
end
Inverse case statement usage
Case branch check state values
Added “full” and parallel case pragmas
Only the next state bit
Onehot FSM Coding Style (Good Style)
5
6
7
8
Notes: Efficient (small and fast) one hot state machine can be coded using an inverse case statement
Full case (// synopsys full_case)
This directive prevents from generating logic to test for any value that is not covered by the case branches and creating an implicit default branch.
Set the full_case directive on a case statement when you know that all possible branches of the case statement are listed within the case statement.
Parallel case (// synopsys parallel_case)
Set the parallel_case directive on a case statement when you know that only one branch of the case statement will be true at a time.
This directive prevents Presto Verilog from building additional logic to ensure the first occurrence of a true branch is executed if more than one branch were true at one time.
The parallel_case statement tells the synthesis tool to not build a priority encoder even though in theory, more than one of the state bits could be set (as engineers, we know that this is a onehot FSM and that only one bit can be set so no priority encoder is required)

## Slide 73: HDL FSM Implementation
Registering the outputs of an FSM design
  Insures that the outputs are glitch-free and frequently
  Improves synthesis results by standardizing the output and input delay constraints of synthesized modules
output reg out1;
parameter [1:0] IDLE=2'b00, BBUSY=2'b01,BFREE=2'b10;
reg [1:0] state, next;
always @(posedge clk or negedge rst_n)
if (!rst_n) state <= IDLE;
else state <= next;
always @(state or in1 or in2) begin
next = 2'bx;
case (state)
IDLE : if (in1) next = BBUSY;
else next = IDLE;
BBUSY: if (in2) next = BBUSY;
else next = BFREE;
endcase
end
always @(posedge clk or negedge rst_n)
if (!rst_n) out1 <= 1'b0;
else begin
out1 <= 1'b0;
case (next)
IDLE, BFREE: ; // default outputs
BBUSY, BWAIT: out1 <= 1'b1;
endcase
end
Registered FSM Outputs (Good Style)

## Slide 74: Verilog for Synthesis

## Slide 75: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 76: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 77: Lexical elements
Case sensitive - keywords are lower case
Semicolons(;) are line terminators
Comments:
  One line comments start with // ...
  Multi-line comments start with /* and end with */
System tasks and functions start with a dollar sign, ex $display, $signed
Notes: System Task are defined by LRM, and provide functionally that can help on the simulation process for example

## Slide 78: Lexical elements
Variable names have to start with an alphabetic character or underscore (_) followed by alphanumeric or underscore characters
Escaped identifiers (\)
  Permit non alphanumeric characters in Verilog name
  The escaped name includes all the characters following the backslash until the first white space character
wire \fo+o=a ; // Declare the varaible fo+o
wire \fo+o =a ; // Assign a to wire fo+o
Notes: For example
wire \fo+o=a ; // Here we are declaring the varible fo+o=a=a
wire \fo+o =a ; // Here we are assigning a to the wire fo+o

## Slide 79: Compiler directives
The directives start with a grave accent ( ` ) followed by some keyword
`define Text-macro substitution
`ifdef, `ifndef, `else, `endif Conditional compilation
`include File inclusion
`include “file1.v”
// Used as `WORD_SIZE in code
`define WORD_SIZE 32
module test ();
`ifdef TEST
// A implementation
`else
// B implementation
`endif
assign out = `WORD_SIZE{1’b1};
endmodule
Notes: Show in the example
The difference usage od the macro
At the `ifdef we don’t include `
But on the macro replacement we include the `

## Slide 80: Reserved keywords
always | and | assign | automatic | begin | buf | bufif0 | bufif1
case | casex | casez | cell | cmos | config | deassign | default
defparam | design | disable | edge | else | end | endcase | endconfig
endfunction | endgenerate | endmodule | endprimitive | endspecify | endtable | endtask | event
for | force | forever | fork | function | generate | genvar | highz0
highz1 | if | ifnone | incdir | include | initial | inout | input
instance | integer | join | large | liblist | library | localparam | macromodule
medium | module | nand | negedge | nmos | nor | noshowcancelled | not
notif0 | notif1 | or | output | parameter | pmos | posedge | primitive
pull0 | pull1 | pulldown | pullup | pulsestyle_ onevent | pulsestyle_ ondetect | rcmos | real
realtime | reg | release | repeat | rnmos | rpmos | rtran | rtranif0
rtranif1 | scalared | showcancelled | signed | small | specify | specparam | strong0
strong1 | supply0 | supply1 | table | task | time | tran | tranif0
tranif1 | tri | tri0 | tri1 | triand | trior | trireg | unsigned
use | uwire | vectored | wait | wand | weak0 | weak1 | while
wire | wor | xnor | xor |  |  |  | 
Underline = supported by synthesis
Notes: Not all of them are supported by synthesis
The lenguage doesn’t allow varaible/module name with this words (this are reserved words)
The ones in blue are supprted by synthesis

## Slide 81: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 82: Logical values
A bit can have any of these values
  0 representing logic low (false)
  1 representing logic high (true)
  X representing either 0, 1, or Z
  Z representing high impedance for tri-state (unconnected inputs are set to Z)
Notes: X in synthesis is don’t care let the synthesis tool do optimizations
X in simulation is unknown

## Slide 83: Logical values
Logic with multilevel (0,1,X,Z) logic values
  Nand anything with 0 is 1
  Nand two X get an X
True tables define the how outputs are compute
& | 0 | 1 | X | Z
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | X | X
X | 0 | X | X | X
Z | 0 | X | X | X
¦ | 0 | 1 | X | Z
0 | 0 | 1 | X | X
1 | 1 | 1 | 1 | 1
X | X | 1 | X | X
Z | X | 1 | X | X
Notes: What happens with X in synthesis?
This are elements that can be optimize, pick the value that helps to optimize the circuit
LRM have the true tables for all the operations
Show the example tables

## Slide 84: Number representation
<size>'<base format><number>
<size>:
  number of bits (optional)
<base format>:
  It is a single character ' followed by one of the following characters b, d, o and h, which stand for binary, decimal, octal and hex, respectively.
<number>
  Contains digits which are legal for the <base format>
  ‘_’ underscore can be use for readability
Notes: Why we would like to define a size of the numer representation?

## Slide 85: Number representation
Negative numbers are store as 2’s complement
Extended number
  If MSB is 0, X or Z number is extended to fill MSBs with 0, X, Z respectively
  If MSB is 1 number is extend to fill MSBs with 0/1, depending on the sign
  3’b01=3’b001 3’bx1=3’bxx1 3’bz=3’bzz
  3’b1=3’b001 -3’b1=-3’b01=3’b111
Notes: From VCS (Extended numbers)
5'b1 = 00001
-5'b1 = 11111
5'b1x = 0001x
-5'b1x = xxxxx
-5'b01 =11111

## Slide 86: Number representation
Unsized numbers (at least 32 bit)
549 // decimal number
'h8F_F // hex number
'o765 // octal number
Size numbers
4'b11 // 4-bit binary number 0011
3'b10x // 3-bit binary number with LSM bit unknown
8'hz // 8-bit binary high-impedance number
4'hz1 // 4’bzzz1
5'd3 // 5-bit decimal number
Signed numbers
-8'd6 // 8-bit two's complement of 6 (-6)
4'shF // 4-bit number ‘1111’ to be interpreted as
// 2’s complement number
Notes: Note
For the negatives numbers
-8’d6=8’b11111010
4’shF=4’b1111 = -1
The others weird number definitions:
8'h0F = 8’b00001111
8'hF = 8’b00001111
8'hz = 8’bZZZZZZZZ
8'h0z = 8’b0000ZZZZ
8'h0x = 8’b0000XXXX
8'hx = 8’bXXXXXXXX

## Slide 87: Data types (reg)
A reg (reg) stores its value from one assignment to the next (model data storage elements)
  Don’t confuse reg with register
  Default value is X
  Default range is one bit
  By default are unsigned, but can be declare signed, using keyword signed
Notes:   Don’t read a reg as a register!!

## Slide 88: Data types (Nets)
Nets (wire) correspond to physical wires that connect instances
  Nets do not store values
  Have to be continuously driven
  The default range is one bit
  By default are unsigned
The wire declaration is used most frequently, other net types are wand, wor, tri, triand, trior, etc.
Notes:   Don’t read a reg as a register!!
  Other wire type:
tri :
Denotes nets that have multiple drivers
Is there are 2 signal of appositive values, the results is X
wor, wand, trior, triand
Performs operations
wand: (and operation) if any value is 0, the value of the net is 0
wor: (or operation) if any value is 1, the value of the net is 1
trior, triand have the same functionality as wor, wand

## Slide 89: Other data types
Integer (integer)
  Convenient to counting purposes
  At least 32-bit wide
  Useful for loop
Real (real) simulation only
  Can be specified in decimal and scientific notation

## Slide 90: Verilog vectors
Know as BUS in hardware
Declare by a range following the type
<data type> [left range : right range] <Variable name>
Single element that is n-bits wide
  reg [0:7] A, B; //Two 8-bit reg with MSB as the 0th bit
  wire [3:0] Data; //4-bit wide wire MSB as the 4th bit
Vector part select (access)
  A[5] // bit # 5 of vector A
  Data[2:0] // Three LSB of vector Data
Vector operation
  B = 32 + A;
Notes: [0:7] Big endian notation
[7:0] Little endian notation
Shows that I can actually operate 2 vectors
This is a Systmet verilog packed array
It is possible to operate element write in little and big endian, but is not recomeneded

## Slide 91: Verilog arrays
Array: range follows the name
<data type> <array name> [<array indices>]
reg B [15:0]; // array of 16 reg elements
Array of vectors
<data type> [<vector indices>]<array name>[<array indices>]
reg [15:0] C [1023:0]; // array of vectors
Memory access
<var name>[<array indices>] [<vector indices>]
Notes: Array is a collection
Vectors : single element that is n-bits wide
Array: Multiple elements that are 1-bit or n-bits wide
Multi-dimentional arrays can be declared with any number of dimensions

## Slide 92: Data storage and Verilog arrays
module RAM (output [7:0] Obus,
input [7:0] Ibus,
input [3:0] Adr,
input Clk, Read
);
reg [7:0] Storage [15:0];
reg [7:0] ObusReg;
assign Obus = ObusReg;
always @(posedge Clk)
if (Read==1’b0) Storage[Adr] = Ibus;
else ObusReg = Storage[Adr];
endmodule
Simple RAM Model
Notes: module RAM (
output [7:0] Obus, // Vector 8 bit-wide
input [7:0] Ibus, // Vector 8 bit-wide
input [3:0] Adr, // Vector 3 bit-wide
input Clk, Read
);
reg [7:0] Storage[15:0]; // Array of Vectors // (16 elements of 8 bits)
reg [7:0] ObusReg;
assign Obus = ObusReg; // Vector assignment
always @(posedge Clk)
if (Read==1’b0)
Storage[Adr] = Ibus; // Vector assignment to one elements
//from the array of vectors
else
ObusReg = Storage[Adr];
endmodule

## Slide 93: Data storage and Verilog arrays
module cter (input rst, clock, jmp,
input [7:0] jump,
output reg [7:0] count
);
always@(posedge clock)
begin
if (rst) count = 0;
else if (jmp) count = jump + count;
else count = count + 1;
end
endmodule
Counter
Notes: module cter (input rst, clock, jmp,
input [7:0] jump, // vectors (bus) as ports
output reg [7:0] count
);
always@(posedge clock)
begin
if (rst) count = 8’h00;
else if (jmp) count = jump + count; // Operations with vectors
else count = count + 8’h1;
end
endmodule

## Slide 94: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 95: Structures and Hierarchy
Hierarchical HDL structures are achieved by defining modules and instantiating modules
top.v
comp.v
mux.v
Notes: Module TOP instantiate ALU and MEM designs are name U1 and U2…
This is one of the most importan elemetns, since it enable the creation of more complex designs

## Slide 96: Module declaration
module <module name> #(<param list>) (<port list>);
<Declarations>
<Instantiations>
<Data flow statements>
<Behavioral blocks>
<Task and functions>
endmodule
Notes: Module is the basic element.
<module name>: is an identifier that uniquely names the module.
#(<parameter list>) parameter are optional
<port list> : is a list of input, inout and output ports which are used to connect to other modules.
<declarations>: section specifies data objects as registers, memories, wires and parameters, port list declarations
<Data flow statements> : assign
<Instantiations> : instantiation off lower level modules
<Behavioral blocks> describe behavior, inside always or initial block
<task and functions>: task and function declarations

## Slide 97: Module header
Start with module keyword, contains the I/O ports
Port declarations begins with output, input or inout follow by bus indices
Each directions are followed by one or more I/O names
Each declaration is separated by comma (,)
module ALU (output [15:0] res,
output cout,
input [15:0] A, B,
input clock, ena);
Notes: Notes:
Bus indices are needed when the size of the ports are more than 1 bit width
Module header ends with ;
Also parameters can be defined

## Slide 98: Port declaration
input and inout are declared as wire
outputs port can be declared wire as reg (holds a value)
2 flavors for port declaration:
module S1 (a, b, c, d, e);
input [1:0] a, b;
input c;
output reg [1:0] d;
output e;
//Verilog 1995 Style
endmodule
module S2 (input [1:0] a, b,
input c,
output reg [1:0] d,
output e);
//ANSI C Style
endmodule
Notes: Verilog -1995 is other way that is repetitive
Verilg-2001 (Ansi-C) defines the directions in the module header

## Slide 99: Parameters
Parameters are means of giving names to constant values
The values can be overridden when the design is compiled
Parameters cannot be used as variables
Syntax
parameter <name> = <constant expression>;

## Slide 100: Parameter declaration
Default value need to be set at declaration time
32 bit wide by default, but may be declared of any width
2 declaration flavors:
Inside a module In module header
module test (... I/O’s ...);
parameter ASIZE = 32, BSIZE =16;
//...
reg [ASIZE -1:0] Abus, Zbus;
wire [BSIZE-1:0] Bwire;
//...
endmodule
module test
#(parameter ASIZE = 32, BSIZE =16)
(... I/O’s ...);
//...
reg [ASIZE -1:0] Abus, Zbus;
wire [BSIZE-1:0] Bwire;
//...
endmodule
parameter [2:0] IDLE = 3’d0;
Notes: Show what can be done with the parameters, for example set the size of inputs
How do you think the instantiation is done now

## Slide 101: Parameter example
Adder
N-bits (8 by default)
reg-ouputs
A[N-1:0]
B[N-1:0]
S[N-1:0]
Cout
Cin
Clk
ANSI C style
module Adder (A, B, Cin, S,Cout, Clk);
parameter N=8;
input [N-1:0]A, B;
input Cin;
input Clk;
output [N-1:0] S;
output Cout;
reg [N-1:0] S;
reg Cout;
//module internals
endmodule
module Adder #(parameter N=8)
(input [N-1:0]A, B,
input Cin,
input Clk,
output reg [N-1:0] S,
output reg Cout
);
//module internals
endmodule
Verilog 95 Style
Notes: N by default is 8
Registered ouputs

## Slide 102: Structures and Hierarchy
Instance of a module
  Instantiation is the process of “calling” a module
  Create objects from a module template
<module name> #(<parameter list>)
<instance name> (<port list>);
Where:
  <module name> Module to be instantiated
  <parameter list> Parameters values passed to the instance
  <instance name> Identifies the instance of the module
  <port list> Port list connection

## Slide 103: Port List Connections
Ports list connections
  Provide the interface by which a module can communicate with the environment
  Port declarations (input, output, inout)
net
net
net
reg or net
net
reg or net
input
output
inout
Notes: By default ports are declares as wire
Is legal to connect element with different sizes on port connections
Port declaration can be done in the declaration section or in the port list definition
Inputs:
  Internally must be of net data type (e.g. wire)
  Externally the inputs may be connected to a reg or net data type
Outputs:
  Internally may be of net or reg data type
  Externally must be connected to a net data type
Inouts:
  Internally must be of net data type (tri recommended)
  Externally must be connected to a net data type (tri recommended)

## Slide 104: Port connections/Parameter overwrite
Named connection
  Explicitly linking the 2 names for each side of the connection
my_mod #(.N(4)) U1 (.in1(a), .in2(b), .out(c));
Order connection
  Expression shall be listed in the same order as the port declaration
my_mod #(4) U2 (a, b, c);
Notes: Ask how to leave a port unconnected
ANS:
my_mod U1 (.in1(a), .in2(), .out(c));
my_mod U2 (a, , c);

## Slide 105: Hierarchy Example
module TOP (input t1, t2, t3, output t4, t5, t6);
wire w1, w2, w3;
ALU #(.S(2)) U1 (.a1(t1), .a2(t2), .a3(t3), .a4(w1), .a5(w2), .a6(w3));
MEM U2 (w1, w2, w3, t4, t5, t6);
endmodule
module ALU (input a1, a2, a3, output a4, a5, a6);
parameter S=4;
reg rsl;
wire sig;
FIFO S1 (.f1(rsl), .f3(sig));
//...
endmodule
module FIFO #(parameter F=2)
(input f1, output reg f2);
//...
endmodule
TOP
ALU
MEM
FIFO
U1
U2
S1
Notes: Module TOP instantiate ALU and MEM designs are name U1 and U2…

## Slide 106: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 107: Relational operators
Mainly use in expression (e.g. if sentences)
Returns a logical value (1/true 0/false)
If there are any X or Z bit returns X (false on a expression)
< | a < b | // is a less than b?
> | a > b | // is a greater than b?
>= | a >= b | // is a greater than or equal to b
<= | a <= b | // is a less than or equal to b
Notes: Relational Operators return 1-bit true/false

## Slide 108: Arithmetic operators
Binary operators
  Takes 2 operators
Unary operators (+/-)
  Specify the sign of the operand
  Negative numbers are represented as 2’s complement
* | c = a * b ; | // multiply a with b
/ | c = a / b ; | // int divide a by b
+ | sum = a + b ; | // add a and b
- | diff = a - b ; | // subtract b from a
% | amodb = a % b ; | // a mod(b)
Notes: What happens if one of the elements have a X
Simulation, the entire expression is X
Synthesis, may be optimize

## Slide 109: Logical operators
Logical operators evaluate to a 1-bit value
If an operand is not zero is treat as logical 1
If an operand is Z o X is treat as X (false)
&& | a && b ; | // is a and b true? returns 1-bit true/false
¦¦ | a ¦¦ b ; | // is a or b true? returns 1-bit true/false
! | if (!a) c = b; | // if a is not true assign b to c
A=3; B=0;
A&&B //Evaluates to 0 same to (logical-1 && logical-0)
!B //Evaluates to 1 same to (!logical-0)
A=2’b0x; B=2’b10;
A&&B //Evaluates to x same to (x && logical-0)
Notes: Returns 1 bit

## Slide 110: Equality and Identity operators
== | c == a ; | /* is c equal to a returns 1-bit true/false applies for 1 or 0, logic equality, using X or Z operands returns always false ('hx == 'h5 returns 0) */
!= | c != a ; | // is c not equal to a, returns 1-bit true
=== | a === b ; | // is a identical to b (includes 0, 1, x, z)
!== | a !== b ; | /* is a not identical to b returns 1-bit true/false*/
Notes: === and !== do a bit by bit comparison

## Slide 111: Bitwise and Reduction operations
& | b = &a ; | /* AND all bits of a (reduction) */
¦ | b = ¦a ; | /*OR all bits (reduction)*/
^ | b = ^a ; | /*Exclusive or all bits of a (reduction)*/
~&,~¦,~^ | c = ~& b ; | /* NAND, NOR, EX-NOR all bits together */
~,&,¦,^ | b = ~a ; e = b ¦ a | /*bit-wise NOT, AND, OR, EX-OR*/
~&,~¦,~^ | e = a ~^ b ; | /*bit-wise NAND, NOR, EX-NOR*/

## Slide 112: Shift and other operator
<< | a << 1 ; | // shift left a by 1-bit
>> | a >> 1 ; | // shift right a by 1
<<< | b <<< 1 ; | // arithmetic shift by 1
>>> | b >>> 1 ; | // arithmetic shift by 1
?: | c = sel ? a : b ; | /* if sel is true c = a, else c = b , ?: ternary operator */
{} | {co, sum} = a + b + ci; | /* add a, b, ci assign the overflow to co and the result to sum: operator is called concatenation */
{{}} | b = {3{a}} | /* replicate a 3 times, equivalent to {a,a,a} */

## Slide 113: Operators precedence
Unary, Multiply, Divide, Modulus | +,-,!,~ | Highest
 | *, / % | 
Add, subtract, shift | +, - | 
 | <<. >> | 
Relational Equality | <, < =, >, >= | 
 | =, ==. != | 
 | ===, !== | 
Reduction Logical | &, ~& | 
 | ^, ^~ | 
 | ¦, ~¦ | 
 | && | 
 | ¦¦ | 
Conditional | ?: | Lowest
Operator precedence
Notes: Always you can use the extra () to be sure

## Slide 114: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 115: Concurrent blocks
Blocks of code with no well-defined order relative to one another
  Module instance is the most important concurrent block
  Continuous assignments are concurrent within a module
  Procedural blocks are concurrent within a module
module AND (input A, B, output C);
wire w;
NAND U1 (A, B, w);
NAND U2 (w, w, C);
endmodule
Notes: For example verilog source file can be compiled in a specific order, but it doesn’t define the order of simulation
Typo it should say
  Continuous assignments, and procedural blocks are concurrent within a module

## Slide 116: Continuous assignments
Continuous assignments imply that whenever any change on the RHS of the assignment occurs, it is evaluated and assigned to the LHS
Continuous assignments always implement combinational logic
Continuous assignments drive wire variables
wire A;
assign A = (B|C)&D;
Notes: Delays are ignore on synthesis

## Slide 117: Continuous assignments
Implicit continuous assignment
  Continuous assignment can be placed when the net is declared
Implicit net declaration (not recommended)
  If a signal name is used to the left of a continuous assignment, a implicit net declaration will be inferred
wire A = i1 & i2;
wire i1, i2;
assign A = i1 & i2;

## Slide 118: Example
A
B
C
A
B
C
module NAND (A, B, C);
input A, B;
output C;
// Continuous assignments
assign C = ~(A&B);
endmodule
module AND (A, B, C);
input A, B;
output C;
wire w;
// 2 NAND instantiations
NAND U1 (A, B, w);
NAND U2 (w, w, C);
endmodule

## Slide 119: Procedural blocks
Each procedural block represent a separate activity flow in Verilog
Procedural blocks
  always blocks
    Model a block of activity that is repeated continuously
  initial blocks simulation only
    Model a block of activity that is executed at the beginning
Multiple behavioral statements can be grouped using keywords begin and end
Notes: Verilog is a concurrent programming language
C is sequential in nature
Each procedural block represent a separate activity flow in Verilog

## Slide 120: Procedural assignments
Procedural assignment changes the state of a reg
Used for both combinational and sequential logic inference
All procedural statements must be within always (or initial) block
reg A;
always @ (B or C)
begin
A = ~(B & C);
end

## Slide 121: Always block – Event control (@)
Always blocks model an activity that is repeated continuously
@ can control the execution
  posedge or negedge make sensitive to edge
  @* / @(*), are sensitive to any signal that may be read in the statement group
  Use “,”/or for multiple signals
Notes: Sensitivity list options
always @* // looks for any changes in the variables read inside the always block
always @ (event)
always @ (event1 or event2)
always @ (event1 , event2) // same as or was introduce en 2001
always @ (event1 and event2) // Not allowed

## Slide 122: Always block – Event control (@)
module M1 (input B, C, clk, rst, output reg X, Y,Z);
// controlled by any value change in B or C
always @ (B or C)
X = B & C;
// Controlled by positive edge of clk
always @(posedge clk)
Y = B & C;
// Controlled by negative edge of clk or rst
always @(negedge clk, negedge rst)
if (!rst) Z = 1’b0;
else Z = B | C;
endmodule
Notes: This is the first slide where the if and else is show, explain a little bit

## Slide 123: Example
G
D
Q
R
D
Q
module FFD (input Clk, R, D,
output reg Q);
always @ (posedge Clk)
begin
if (R)
Q = 1'b0;
else
Q = D;
end
endmodule
module LD (G, D, Q);
input G, D;
output Q;
reg Q;
always @ (G or D)
if (G)
Q = D;
endmodule
Notes: DFF has a synchronous reset
How we can transform this to an asynchronous reset DFF?
If the sensitivity list is like this “always @ (posedge Clk or positive R)” the DFF has an asynchronous reset

## Slide 124: Blocking / Non-Blocking assignment
Blocking assignment
(= operator) acts much like in traditional programming languages
The whole statement is done before control passes on to the next statement.
Non-blocking assignment
(<= operator) Evaluates all the right-hand sides for the current time unit and assigns the left-hand sides at the end of the time unit.
always @(posedge Clk)
begin
//blocking procedural assignment
C = C + 1;
A = C + 1;
end
always @(posedge Clk)
begin
//non-blocking procedural assignment
D <= D + 1;
B <= D + 1;
end
Example: During every clock cycle
A is ahead of C by 1
B is same as D
Notes: ASK: Which are the values of A and C; and D and B!
HERE
Agregar un dibujo con la inferencia de registros que se obtiene

## Slide 125: Blocking/Non-Blocking example
module t (input clk, A,
output reg B, C);
always @(posedge clk)
begin
B <= A;
C <= B;
end
endmodule
module t (input clk, A,
output reg B, C);
always @(posedge clk)
begin
B = A;
C = B;
end
endmodule
DFF
CLK
A
B
C
DFF
D
Q
D
Q
DFF
CLK
A
B
C
D
Q
Notes: Non-blocking: is like taking a picture B and C willl have the value of the registers (B and C will be updated at the same time)
Blocking: C will be updated after B is update, so they have the same value

## Slide 126: Procedural blocks (summary)
Blocks of code within a procedural block are read (simulated, executed) in order
Procedural blocks may contain:
  Blocking assignments
  Non-blocking assignments
  Procedural control statements (if, for, case)
  function, or task calls
  Event control (‘@’)
  Nested procedural blocks enclosed in begin … end
Notes: REVIEW

## Slide 127: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 128: Conditional statements (if … else)
The statement occurs if the expressions controlling the if statement evaluates to true
  True: 1 or non-zero value
  False: 0 or ambiguous (X)
  Explicit priority
always @ (WRITE or STATUS)
begin
if (!WRITE)
begin
out = oldvalue;
end
else if (!STATUS)
begin
q = newstatus;
end
end
if (<expression>)
// statement1
else if (<expression>)
// statement2
else
// statement3
Notes: The expression is considered to be true is it non-zero, and false if it zero, X, or Z

## Slide 129: Conditional statements (case)
case, casex, casez: case statements are used for switching between multiple selections
  If there are multiple matches only the first is evaluated
  Breaks automatically
casez treats Z as don’t care
casex treats Z and X as don’t care
case (<expression>)
<alternative 1> : <statement 1>;
<alternative 2> : <statement 2>;
default : <default statement>;
endcase
Notes: Case statement compared 0, 1, x, z values in the expression and the alternatives bit for bit

## Slide 130: Conditional statements (case)
always @(s, a, b, c, d)
case (s)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
2'b11: out = d;
endcase
always @*
casex (state)
/*
during comparison : 3'b01z,
3'b01x, 3b'011 ... match case
3'b01x
*/
3'b01x: fsm = 0 ;
3'b0xx: fsm = 1 ;
default: fsm = 1 ;
endcase
always @*
casez (state)
// 3'b11z, 3'b1zz,... match 3'b1??
3'b1??: fsm = 0;
3'b01?: fsm = 1;
endcase
Notes: always @* is a verilog-2001 feature
is it possible to do something similar with if sentences
Answer ==! and ===
Notes:
- if in one case have 2 or more branch that are the same option the first one will be use

## Slide 131: Example
out
s[0]
d
c
b
a
s[1]
8-bit
4-to-1
multiplexer
module mux(a, b, c, d, s, out);
input [7:0] a, b, c, d;
input [1:0] s;
output [7:0] out;
reg [7:0] out;
// used in procedural statement
always @ (s or a or b or c or d)
case (s)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
2'b11: out = d;
endcase
endmodule

## Slide 132: Latches / Muxes (Comb logic)
Assuming only level sensitivity on a always block:
  A variable or signal when is fully specified (it is assigned under all possible conditions) a mux or combinational logic.
  If a variable or signal is not fully specified a latch will be inferred
always @ (a,b,sel) if (sel==1’b1) z=a; else z=b; | always @ (DATA, GATE) if (GATE) Q = DATA; | always @ (DATA, GATE) begin Q = 0; if (GATE) Q = DATA; end
MUX
COMB LOGIC
LATCH
Notes: ASK which are the 3 blocks MUX/LATCH/COMB LOGIC
Assuming only level sensitive (no edge sensitivity)
Mux can be implemented as combinational logic
The last case will depend on the synthesis tool behavior
MUX: if-else is fully specified
LATCH: what happens if GATE is 0, nobody know, so the tools creates a latch to keep that value
COMB LOGIC: is like a mux, but the coding style doesn’t infer a MUX, this depends on the Synthesis tools

## Slide 133: Loop statements (for)
Works the same ways as C
Unary increment/decrement is not allowed
for (<loop var init>; <loop var reentry expr>; <loop var update>)
<statement>;
// General purpose loop
interger i;
always @*
for (i=0 ; i<=7 ; i=i+1)
memory[i] = 0;
Notes: Repeat is not supported by synthesis

## Slide 134: Loop statements (while)
Loop execute until the expression is not true
always @*
while(delay)
// Multiple statement groups with begin-end
begin
ldlang = oldldlang;
delay = delay – 1;
end

## Slide 135: Loop statements (repeat)
Repeat statement a specified number of times
The number is evaluated only at the beginning
always @*
repeat(`BIT-WIDTH)
begin
if (a[0]) out = b + out;
a = a << 1;
end
Notes: What happens if the number that control the repeat loop is not a constant? Synthesis /simulation differences?

## Slide 136: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 137: Tasks and Functions
Task
  Declare with task and endtask
  May have zero arguments or more arguments of type input, output, inout
  Do not return with a value, can pass values through output and inout arguments
Functions
  Declare with function and endfunction
  Must have at lease one input
  Always return a single value (cannot have output or inout arguments)
Task and function serve the same purpose on Verilog as subroutines do in C

## Slide 138: Tasks and Functions - example
module top (input a1, a2, output reg [1:0] b1, b2);
always @ (a1, a2)
begin
b1 = out (a1, a2); // Function calling
out_task (a1, a2, b2); // Task calling
end
function [1:0] out (input in1, in2); // Function Declaration
begin
if (in1) out = {in2,in1}; else out = {in1,in2};
end
endfunction
task out_task (input in1, in2, output [1:0] out); // Task Declaration
begin
if (in1) out = {in2,in1}; else out = {in1,in2};
end
endtask
endmodule

## Slide 139: Task and Functions
Functions are simpler
Data Sharing
  Functions and task could be declare as automatic
  A static function retains the value of all it's internal variables between calls. An automatic function re-initializes them each call
Function | Task
Can call another function | Can call another function or task
Can modify only one value | Can modify multiple values
Notes: I terms of synthesis, a static function requires state elements (probably latches), while an automatic call is purely combinational
I terms of simulation, a static function allow recursive functions
function automatic [63:0] factorial;
input [31:0] n;
if (n == 1)
factorial = 1;
else
factorial = n * factorial(n-1);
endfunction

## Slide 140: Outline
Lexical elements
Data type representation
Structures and Hierarchy
Operators
Blocks and Assignments
Control statements
Task and functions
Generate blocks
Notes: Lexical elements: see lexical elements related to the language, line terminations, identifiers, keywords, compiler directives
Structures and Hierarchy: study the basic Verilog element module and how instantiate designs
Assignments: study how to assign variables, will see continuous assignments and procedural assignments
Data type: representation see data types and numbers representations
Operators: see available operators
Control statements: Control elements like if, case, for, etc.
Task and functions: task and function construct to simplify code
Generate blocks: to dynamic generate code

## Slide 141: Generate blocks
Allow to generate Verilog code dynamically at elaboration time
  Facilitated the parameterized model generation
  Required the keywords generate – endgenerate
  Generate instantiations can be
    Module instantiations
    Continuous assignments
    initial / always blocks
  Typically used are generate loop and conditional generate

## Slide 142: Generate loop
module top( input [0:3] in1,
output [0:3] out1);
// genvar control the loop
genvar I;
generate
for(I=0; I<=3; I=I+1 )
begin
sub U1 (in1[I], out1[I]);
end
endgenerate
endmodule
Notes: 4 copies of design sub will be place
The naming standard is defined in the LRM
The genvar reserved word is used as the index control variable by generate for loops

## Slide 143: Conditional generate
module top #(parameter POS=0)
(input in, clk, output reg out);
generate
if(POS==1)
always @ (posedge clk)
out = in;
else
always @ (negedge clk)
out = in;
endgenerate
endmodule