## Slide 1: Verilog Lab I

## Slide 2: Lab 1 – 1 bit full adder
Use Karnaugh Map to derive logic expression for the addition.
Create the file OneBitAdder.v
  Write the Verilog code that implements binary addition operation based on the expression obtained previously
Use the following interface
a | b | cin | sum | cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
1 module onebitadder (
2 input a, b, cin,
3 output sum, cout
4 );

## Slide 3: Lab 1 – 1 bit full adder - Answer
Your design should implement the following netlist:
Logic expressions:
1 module onebitadder (
2 input a, b, cin,
3 output sum, cout
4 );
5
6 assign sum = a^b^cin;
7 assign cout = a&b | a&cin | b&cin;
8
9 endmodule

## Slide 4: Lab 2 – Basic modules
This lab will consist on creating some basic designs (modules).
A description of the design functionality will be provided.
The objective is to translate the description into a synthesizable Verilog code.
It is very important to use the module interface that will be provided.
In order to do a syntax check on the Verilog code written, vlogan tool can be used. The following line can be executed on the shell
vlogan <verilog_file.v> –full64 –sverilog +v2k

## Slide 5: Lab 2a – Parameterized 4-input MUX
Write the Verilog code that implements a 4-input multiplexer (mux) with variable (parameterized) input and output bus width.
Use the following interface
1 module mux4 #(
2 parameter WIDTH= 8
3 ) (
4 input [WIDTH-1:0] din1, din2, din3, din4,
5 input [1:0] select,
6 output [WIDTH-1:0] dout
7 );
din1
din2
din3
din4
select
dout

## Slide 6: Lab 2b – Parameterized Register Bank
Write the Verilog code that implements a D-type Register Bank with parameterized depth. It should:
  Operate on positive edge of the clock (clk)
  Have a Synchronous reset (rst)
  Have an enable signal (wr_en) which allows data capturing only when asserted.
Use the following interface
1 module register_bank #(
2 parameter WIDTH = 8
3 ) (
4 input [0:0] clk,
5 input [0:0] rst,
6 input [0:0] wr_en,
7 input [WIDTH-1:0] in,
8 output [WIDTH-1:0] out
9 );
in[0]
in[1]
in[2]
in[3]
out
clk
in[4]
in[5]
in[6]
in[7]
rst
wr_en
8

## Slide 7: Lab 2c – Parameterized 4-input MUX with output register
Write the verilog code that implements a 4-input multiplexer (mux) with a variable (parameterized) input and output bus width, and synchronous output.
Use the following interface
1 module mux4_registered #(
2 parameter WIDTH= 8
3 ) (
4 input [0:0] clk,
5 input [0:0] rst,
6 input [1:0] sel,
7 input [WIDTH-1:0] in1, in2, in3, in4,
8 output [WIDTH-1:0] out
9 );
in1
in2
in3
in4
sel
out
clk
rst

## Slide 8: Lab 2c – Basic ALU
Write the Verilog code for a basic ALU module (Arithmetic Logic Unit).
  This ALU has to have addition, subtraction, multiplication and division operations.
    It should have two variable (parameterized) width inputs and output bus in accordance.
    Signal zero[0] should be asserted when the result of the current operation is 0.
    Signal error[0] should be asserted when dividing by 0 is attempted or when input data is not valid.
      On error condition, output must be forced to be -1
  Operations should be described using Verilog arithmetic operators.
Use the following interface
1 module ALU #(
2 parameter WIDTH = 8
3 ) (
4 input [WIDTH-1:0] in1, in2,
5 input [3:0] op,
6 input [0:0] nvalid_data,
7 output [2*WIDTH-1:0] out,
8 output [0:0] zero,
9 output [0:0] error
10 );