## Slide 1: Verilog Lab II

## Slide 2: Lab 3 - Simulation
This lab will be focused on simulating each module created in Lab 2 (a, b, c)
  Simulations will be done using VCS tool.
For labs 2a, 2b and 2c:
  Write a test bench for each module.
  Simulate them in VCS.
vcs –full_debug –sverilog <testbench_file.sv> <verilog_file.v>

## Slide 3: Lab 4 – Full design
The objective is to create a basic multicycle processor as shown in the diagram below.
  Modules previously designed should be used. (Mux, ALU, Regbank)

## Slide 4: Lab 4 – Full design (cont.)
Specifications of the design:
  This is a multicycle processor (3 stages) with no pipelining.
  It has 3 variable with input buses to be used as operands.
  The ALU has 2 multiplexed inputs:
    Each MUX is feed by the 3 input buses and the ALU output.
    Details on how to control the ALU are available in Lab 2d.
  Both reset (rst) and clock (clk) signals should be connected to every module that uses them.
  It has a control unit feed by a 6 bit word (cmdin). This control unit has to:
    Enable the register stages only when applicable
    Select the outputs of each MUX
    Provide the control signals for the ALU.
      Inverted valid data signal must be asserted when data is feed from the feedback loop and the previous result was not valid (Error condition)
      OPCODE to select the operation performed by the ALU.

## Slide 5: Lab 4 – Full design (cont.)
The control block shall be designed to implement the following Instruction Set Architecture (ISA):
The opcode bus should be decoded according to the following table:
opcode[1] | opcode[0] | Operation
0 | 0 | Add
0 | 1 | Sub
1 | 0 | Mul
1 | 1 | Div
5 | 4 | 3 | 2 | 1 | 0
muxA
muxB
opcode
cmdin

## Slide 6: Lab 4 – Full design (cont.)
The control module
  Write the Verilog code for implementing this module based on the details and ISA provided previously.
  Write a test bench to validate this module. It should cover all possible operations, corner cases and exercise all outputs.
  Its interface should be as follows:
1 module control (
2 input wire [0:0] clk,
3 input wire [0:0] rst,
4 input wire [5:0] cmd_in,
5 input wire [0:0] p_error,
6 output reg [0:0] aluin_reg_en,
7 output reg [0:0] datain_reg_en,
8 output reg [0:0] aluout_reg_en,
9 output reg [0:0] nvalid_data,
10 output wire [1:0] in_select_a,
11 output wire [1:0] in_select_b,
12 output reg [4:0] opcode
13 );

## Slide 7: Lab 4 – Full design (cont.)
Full design
  Write the Verilog code that implements this simple microprocessor. At this point it is mostly about connecting together all the modules created so far.
  A test bench will be provided.
  Its interface should be as follows
1 module top #(
2 parameter WIDTH= 8
3 ) (
4 input wire [0:0] clk,
5 input wire [0:0] rst,
6 input wire [5:0] cmdin,
7 input wire [WIDTH-1:0] din_1,
8 input wire [WIDTH-1:0] din_2,
9 input wire [WIDTH-1:0] din_3,
10 output wire [WIDTH-1:0] dout_low,
10 output wire [WIDTH-1:0] dout_high,
10 output wire [0:0] zero,
10 output wire [0:0] error
11 );